## Slide 1: DIGITAL SYSTEM & BINARY NUMBERS
By :
Abdul Ghofir, M.Kom

## Slide 2: Digital System
Digital systems are designed to store, process, and communicate information in digital form.
A computer manipulates information in digital, or more precisely, binary form.
A binary number has only two discrete values — zero or one.
Each of these discrete values is represented by the OFF and ON status of an electronic switch called a transistor.

## Slide 3: Binary Digital Signal
Binary values are represented abstractly by:
  Digits 0 and 1
  Words (symbols) False (F) and True (T)
  Words (symbols) Low (L) and High (H)
  And words On and Off

## Slide 4: Decimal Number System
Base (also called radix) = 10
  10 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 }
Digit Position
  Integer & fraction
Digit Weight
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation

## Slide 5: Octal Number System
Base = 8
  8 digits { 0, 1, 2, 3, 4, 5, 6, 7 }
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation

## Slide 6: Binary Number System
Base = 2
  2 digits { 0, 1 }, called binary digits or “bits”
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Bit x Weight”
Formal Notation
Groups of bits 4 bits = Nibble
8 bits = Byte

## Slide 7: Hexadecimal Number System
Base = 16
  16 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F }
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation

## Slide 8: The Power of 2

## Slide 9: Addition
Decimal Addition

## Slide 10: Binary Addition
Column Addition

## Slide 11: Binary Subtraction
Borrow a “Base” when needed

## Slide 12: Binary Multiplication
Bit by bit

## Slide 13: Decimal (Integer) to Binary Conversion
Divide the number by the ‘Base’ (=2)
Take the remainder (either 0 or 1) as a coefficient
Take the quotient and repeat the division

## Slide 14: Decimal (Fraction) to Binary Conversion
Multiply the number by the ‘Base’ (=2)
Take the integer (either 0 or 1) as a coefficient
Take the resultant fraction and repeat the division

## Slide 15: Decimal to Octal Conversion

## Slide 16: Binary − Octal Conversion
8 = 23
Each group of 3 bits represents an octal digit
Octal | Binary
0 | 0 0 0
1 | 0 0 1
2 | 0 1 0
3 | 0 1 1
4 | 1 0 0
5 | 1 0 1
6 | 1 1 0
7 | 1 1 1
Works both ways (Binary to Octal & Octal to Binary)

## Slide 17: Binary − Hexadecimal Conversion
16 = 24
Each group of 4 bits represents a hexadecimal digit
Hex | Binary
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
A | 1 0 1 0
B | 1 0 1 1
C | 1 1 0 0
D | 1 1 0 1
E | 1 1 1 0
F | 1 1 1 1
Works both ways (Binary to Hex & Hex to Binary)

## Slide 18: Octal − Hexadecimal Conversion
Convert to Binary as an intermediate step

## Slide 19: Decimal, Binary, Octal and Hexadecimal

## Slide 20: Binary Logic
Definition of Binary Logic
  Binary logic consists of binary variables and a set of logical operations.
  The variables are designated by letters of the alphabet, such as A, B, C, x, y, z, etc, with each variable having two and only two distinct possible values: 1 and 0,
  Three basic logical operations: AND, OR, and NOT.

## Slide 21: Binary Logic

## Slide 22: Binary Logic
Truth Tables, Boolean Expressions, and Logic Gates

## Slide 23: Switching Circuits

## Slide 24: Binary Logic
Logic gates
  Example of binary signals

## Slide 25: Binary Logic
Logic gates
  Graphic Symbols and Input-Output Signals for Logic gates:
Symbols for digital logic circuits

## Slide 26: Binary Logic
Logic gates
  Graphic Symbols and Input-Output Signals for Logic gates:
Input-Output signals for gates

## Slide 27: Binary Logic
Logic gates
  Graphic Symbols and Input-Output Signals for Logic gates:
Gates with multiple inputs

## Slide 28: What is the output of Q below?

## Slide 29: How is graphic symbol of Q below?
A = 0111, B = 1100, C = 0101